Press Release WA1401: The SZG81 WDGA draw-wire system

Images and text are approved for publication in the trade press (print and online) in connection with this press release.  Please send us a copy after publication. Thank you in advance for your efforts.

Systematic, absolute length measurement

Precise, yet robust

Robust draw-wire system

Reliable draw-wire system

The precise and very robust SZG81-WDGA draw-wire system from Wachendorff Automation was developed for use in harsh environments.

The various methods of installation mean high flexibility. Wire exit up, down, forward, backward. Thanks to its compact dimensions it can also be used where space is tight.

The draw-wire system can be mounted quickly and with its highly precise mechanics provides reliable and accurate length measurements from 0 mm to 6,250 mm with all advantages, which result from an absolute length measurement. For example, the position value is saved even if the power supply fails and is available immediately once power is restored. This means it is not necessary to perform a reference run and the process can go on without delay. The resolution can be freely configured by the user and changed at any time.

An optimally tuned spring suspension with protection class IP65 and a nylon-coated stainless steel wire cable guarantee a long service life, even

in difficult operating conditions, in a broad temperature range from -40 °C to 80 °C.

An extremely compact and robust absolute encoder of the WDGA family with EnDra® technology is already installed in this system designed as needed for CANopen, SSI or Profibus-DP.

More information: www.wachendorff-automation.com/szg

Picture (Wachendorff):   PI_WA1401_Laengenmesssytem_SZG81 WDGA.jpg

Caption:

The SGZ81-WDGA draw-wire system from Wachendorff Automation is already equipped with a compact and robust absolute encoder of the WDGA family with EnDra® technology, designed for CANopen, SSI or Profibus-DP.

PI_WA1401_draw wire system_SZG81_WDGA.jpg